## Slide 1
www.carteeh.org

## Slide 2: Lecture #55: Alternative and Emerging Technologies—Shared Mobility
Peng Hao
Center for Environmental Research & Technology
University of California, Riverside
Contact information: haop@cert.ucr.edu, 951-781-5777
The author declares that there is no conflict of interest
Lecture Track(s): TT
Notes:   Health Track (HT)—mainly targeted at urban planners, transportation planners, and engineers with limited knowledge of public health-related concepts;
  Transportation Track (TT)—mainly targeted at environmental epidemiologists and public health professionals with limited knowledge of transportation-related concepts; and;
  Planning and Policy Track (PPT)—mainly targeted at planners, civil servants, and policy and decision makers with particular interest in the science-policy link.

## Slide 3: Introduction
Three potentially transformative technologies in transportation sector – connectivity and automation, electrification, and shared mobility.
Shared mobility is innovative transportation strategy that enable short-term access to travel modes on-demand.
Shared mobility applications include car sharing, scooter sharing, bicycle sharing, alternative transit services, ridesharing, transport network companies (TNCs), and courier network service.
There is high uncertainty in forecasting the environmental impact of shared mobility.
Source: Shaheen et al. (2019)
Notes: Transportation activities, including both goods and people movement, have been playing a crucial role in fossil fuel consumption and air pollutant emissions. In 2015, the United States consumed approximitely 97.5 quadrillion BTUs (Quads) of energy, and 28.4% of this was used for transportation purposes. According to the estimation from U.S. Environmental Protection Agency (USEPA), transportation activities were responsible for about 26% of the total U.S. greenhouse gas (GHG) emissions in 2014. Meanwhile, in many areas, vehicle emissions have become the dominant source of air pollutants, including greenhouse gas (GHG), carbon monoxide (CO), volatile organic compound (VOCs), nitrogen oxides (NOx), particulate matter (PM), and polycyclic aromatic hydrocarbons (PAH).
The transportation sector is going through a major revolution with the emergence of three potentially transformative technologies – connectivity and automation, electrification, and shared mobility (Fulton et al., 2017). Connectivity and automation together are the driving force for many applications that promote safety and efficiency of transportation systems (McGuckin et al., 2017). Electrification of transportation systems involves no direct combustion of fossil fuel on-board, and instead relies on electrical grid for fuel. Shared mobility is achieved through sharing single mode of travel among multiple travelers. In addition to the safety and mobility benefits, energy efficiency improvement and emissions reduction are often touted as co-benefits from connected and autonomous vehicles (Rios-Torres & Malikopoulos, 2017). However, proper estimation of emissions reduction benefits is difficult because of uncertainties regarding the final form of technology as well as end user adoption and adaptation rates. Similar uncertainties exist in the estimation of emissions reduction benefits of electrification and shared mobility.

## Slide 4: Shared Mobility and Emissions
Total emissions = # of vehicles × Distance traveled per vehicle × Emission factor
Shared mobility impacts the vehicle ownership and vehicle-miles traveled (VMT).
Bicycle/scooter sharing and alternative transit services, as alternative mode to passenger vehicles, would effectively reduce the vehicle ownership and usage, e.g. 5.5% bike sharing users sold or postponed the car purchase.
Car sharing and ridesharing, also restrain the car ownership and usage and VMT by improving the utilization of vehicle.
Ride-sourcing (i.e. TNC) and has mixed impact on the vehicle usage. They may induce additional travel, but would also extend the catchment area and encourage the use of public transit.
Notes: Traffic-related emissions are a function of total vehicle miles traveled (VMT) and emission factors for the particular pollutant per unit distance. Once released into the air, these emissions are dispersed and exposed by nearby population, potentially affecting their health. The level of exposure to traffic-related emissions and any consequent health impacts depend on several factors such as proximity to major roadways, meteorological conditions, and demographics. Any technological change which increases VMT and/or induce a condition that results in a higher emission factor will lead to an increase in traffic-related emissions. Emission factors depend not only on the specific vehicle under consideration but also on the traffic and environmental conditions under which the vehicle operates. For example, emission factors are often represented as a function of average traffic speed on the roadway link under consideration. Typically, the function has a “U” shape with higher emission factors at very low and very high average speeds.

## Slide 5: Current Situation of TNCs
TNCs is a focal point of our discussion as the current US market share of all the other categories combined is inappreciable compared to that of TNCs.
TNCs such as Uber and Lyft match drivers who subscribe to their platform with trip requests from individuals. Most of the trip requests are from single travelers -the majority of the TNC trips are not shared rides.
  In Boston, the average occupancy rate for TNC trips is 1.5, including the driver (MAPC, 2018).
To promote ridesharing, major TNCs offer shared ride service options such as UberPOOL and Lyft Line in major cities.
However, only a small fraction of users who have access to these shared ride options request them, and even a smaller number of those trip requests are actually matched as shared rides.
Notes: On-demand mobility services involves arranging for travel on-demand. Usually, the travelers request their “rides” on automobile or paratransit using a smartphone app. The service provider typically manages a fleet of vehicles and optimizes the vehicles’ locations and route assignments based on the dynamic demand of subscribers. Greenblatt and Shaheen (2017) classified on-demand mobility services in four major categories – transport network companies (TNCs), carsharing, ridesharing, and e-hailing.
TNCs such as Uber and Lyft match drivers who subscribe to their platform with trip requests from individuals. Most of the trip requests are from single travelers; therefore, the majority of the TNC trips are not shared rides. For example, according to a recent study in Boston the average occupancy rate for TNC trips is 1.5, including the driver (MAPC, 2018). To promote ridesharing, major TNCs offer shared ride service options such as UberPOOL and Lyft Line in major cities. However, only a small fraction of users who have access to these shared ride options request them, and even a smaller number of those trip requests are actually matched as shared rides.
The National Household Travel Survey (NHTS) is the only nationwide data available on the usage of different travel modes including on-demand mobility services in the US. Among the 92,400 reported trips in the 2016-17 NHTS survey, 3,463 were classified as “Taxi/Limo”. The 2017 NHTS survey also indicated that people used their private vehicles less compared to previous years, and instead used ride-hailing options more. According to Lyft submitted prospectus to the US Securities and Exchange Commission (Lyft Inc., 2019), their number of annual rides increased from 162 million in 2016 to 619 million in 2018. A recent article (Gessner, 2019) reported the February 2019 TNC market share of Uber, Lyft, and others at 67.3%, 30.3%, and 2.4% respectively. Thus, the total estimated TNC rides for 2018 in the US is about 2.04 billion.

## Slide 6: Methodology to Study Emission-related Impacts
The traffic-related emissions and the associated air quality, exposure, and health impacts ensue from the underlying need for the movement of people and goods.
We categorize the potential changes in emissions as:
  Change in Exposure Time: the amount of time people spend in the microenvironments impacted by traffic-related emissions.
  Change in Vehicle and Fuel Technologies: any increase or decrease in emissions resulting from a change in the vehicle and/or fuel technologies is likely to impact public health in the same direction
  Change in Short Term Travel Activity: trip-specific decisions such as driving more or less, sharing a ride, choosing a different departure time, and adopting a more efficient driving style.
  Change in Long Term Travel Behavior: lifestyle changes such as foregoing vehicle ownership, moving to a new location, and making new types of trips
Notes: The traffic-related emissions and the associated air quality, exposure, and health impacts ensue from the underlying need for the movement of people and goods. Some of the potential changes in emissions due to the adoption of emerging technologies happen indirectly, at the very root of how people decide to make trips. Other changes affect the level of emissions and their distribution more directly. In this chapter, we categorize the potential changes as follows:
Change in Exposure Time: Exposure time, in the context of this chapter, refers to the amount of time people spend in the microenvironments impacted by traffic-related emissions. Any changes which increase exposure are likely to increase health-related impacts as well. Increased exposure may or may not be a direct result of adopting the technologies.
Change in Vehicle and Fuel Technologies: Any increase or decrease in emissions resulting from a change in the vehicle and/or fuel technologies is likely to impact public health in the same direction, given that there are no changes in exposure time. Changes in these technologies may be different geographically and across time.
Change in Short Term Travel Activity: Changes in short-term travel-related activity resulting from the adoption of emerging technologies may include trip-specific decisions such as driving more or less, sharing a ride, choosing a different departure time, and adopting a more efficient driving style. They do not include long-term travel-related decisions such as mode choice for daily commute and residential location choice.
Change in Long Term Travel Behavior: In addition to the short-term activity changes, the emerging technologies may also induce lifestyle changes that impact travel behavior such as foregoing vehicle ownership, moving to a new location, and making new types of trips. Such long-term changes may have a lesser immediate effect as compared to the other three categories, but the magnitude of the effect in the long run may be significant depending on the technology and the type of behavior influenced.

## Slide 7: Change in Exposure Time
On-demand mobility services, especially those offered by TNCs, operate on a premise that people will not own vehicles and rather use these services to meet their travel needs.
TNC users often spend time by curbside waiting for the vehicles to pick them up.
This could translate to an increase in the amount of time spent in the microenvironment with a higher level of traffic-related air pollution as compared to using personal vehicles.
The extent of the increase in exposure to traffic emissions will depend on a number of factors such as the frequency of service use, the pick-up locations, and the level of traffic emissions at those locations.
Notes: Current TNC operation is primarily based on existing vehicle and fuel technologies and is expected to remain the same in the near future. However, TNCs are likely to be early adopters of fuel-efficient and alternative fuel vehicles as fuel cost accounts for a significant portion of their total operating costs. Hu et al. (2018) studied the potential of replacing New York City taxi trips with TNC services. They found that 94% of the TNC trips required would be shorter than 200 miles. Considering the range of current electric vehicles in the market, TNC drivers can practically switch to electric vehicles.

## Slide 8: Change in Vehicle and Fuel Technologies
TNCs are likely to be early adopters of fuel-efficient and alternative fuel vehicles as fuel cost accounts for a significant portion of their total operating costs.
Hu et al. (2018) found that in NYC 94% of the TNC trips required would be shorter than 200 miles – a good market for electric vehicles
Wenzel et al. (2019) showed that TNC drivers uses more efficient vehicles than average: larger proportion of newer cars, CUVs, and minivans with more efficient powertrains
Source: Wenzel et al. (2019)
Notes: Current TNC operation is primarily based on existing vehicle and fuel technologies and is expected to remain the same in the near future. However, TNCs are likely to be early adopters of fuel-efficient and alternative fuel vehicles as fuel cost accounts for a significant portion of their total operating costs. Hu et al. (2018) studied the potential of replacing New York City taxi trips with TNC services. They found that 94% of the TNC trips required would be shorter than 200 miles. Considering the range of current electric vehicles in the market, TNC drivers can practically switch to electric vehicles.

## Slide 9: Change in Short Term Travel Activity
Optimistic estimate
  Alonso-Mora et al. (2017) found that 98% of the total 14,000 taxi trips could be replaced by 3,000 ride-share vehicles with capacity of 4 passengers per vehicle or 2,000 vehicles with 10 passengers per vehicle.
  Bischoff and Maciejewski (2016) found that a fleet of 100,000 shared autonomous vehicles would be able to serve trips from 1.1 million personal vehicles sufficiently.
Evidence of the real-world
  TNCs can incur a significant amount of “deadhead” miles, which are the miles where the driver is driving without any passenger, such as from the drop-off location of one trip to the pick-up location of the next trip (Wenzel et al. 2019)
  Komanduri et al. (2018) used RideAustin data to estimate that 37% of all the miles are due to deadheading. It was estimated to be around 20% in San Francisco (Castiglione et al, 2018) and about 50% in New York City (Schaller, 2018).
Notes: On-demand mobility services that do not convert non-motorized and transit trips to vehicle trips and that promote ridesharing are expected to reduce the total VMT on the roadways, which would result in a reduction in emissions. Alonso-Mora et al. (2017) compared 14,000 New York City taxi trips with a hypothetical ride-sharing operation. They found that 98% of the total taxi trips could be replaced by 3,000 ride-share vehicles with capacity of 4 passengers per vehicle or 2,000 vehicles with 10 passengers per vehicle. Bischoff and Maciejewski (2016) simulated trips from 1.1 million personal vehicles in the city of Berlin, Germany, and found that a fleet of 100,000 shared autonomous vehicles would be able to serve those trips sufficiently. In these simulation studies, no barriers to the adoption of ride-sharing were assumed and, therefore, they represent an ideal scenario.
Evidence of the real-world impacts of TNCs, especially on VMT and congestion, has begun to emerge recently. In the short term, TNCs can incur a significant amount of “deadhead” miles, which are the miles where the driver is driving without any passenger, such as from the drop-off location of one trip to the pick-up location of the next trip (Wenzel et al. 2019). A recent paper (Komanduri et al. 2018) using RideAustin data estimated that 37% of all the miles are due to deadheading. It was estimated to be around 20% in San Francisco (Castiglione et al, 2018) and about 50% in New York City (Schaller, 2018). Castillo et al. (2018) presented a condition of matching failure by TNCs where there is fewer number of available vehicles nearby than there are trip requests. Such failure may contribute to a substantially increased amount of deadhead miles. The number of these empty passenger trips can be reduced significantly by imposing an adaptive matching radii within which the driver supply and trip demand matching must occur (Xu et al., 2019).

## Slide 10: Change in Long Term Travel Activity
Positive impacts:
  TNCs may reduce the ownership of private cars
  TNCs may complement public transit by providing first and last mile services
  Hall et al. (2018) found that transit ridership decreased by 5.9% in smaller cities but increased by 0.8% in larger cities due to the entry of Uber.
Negative impacts – mode replacement
Source: Wenzel et al. (2019)
Notes: In longer term, TNCs may complement public transit by providing first and last mile services, or decrease transit ridership by competing with it. Hall et al. (2018) found that transit ridership decreased by 5.9% in smaller cities but increased by 0.8% in larger cities due to the entry of Uber. Clewlow and Mishra (2017) surveyed more than 4,000 residents in seven large cities in the US and found that 15% of public transit, 17% walk, and 7% bike trips were replaced by TNC trips, and that induced trips—trips which did not have happened if TNC service was not there—consisted of 22% of the total TNC trips. A similar study by Henao and Marshall (2018) conducted in Denver, Colorado, found that public transit trips replaced by TNCs and induced TNC trips were 22% and 12%, respectively.

## Slide 11: Anticipated Impacts on Emissions and Exposure
Source: Tanvir et al. (2020)
Notes: The different impacts of the three emerging technologies on emissions as discussed in the previous subsections are summarized in Table 1. Although there are many uncertainties in the different types of change, we have used the evidence that has been reviewed along with our best judgment to determine the likelihood, directionality, and magnitude of emissions impact. Three categories of likelihood are used – unlikely, somewhat likely, and extremely likely. The directionality is positive if emissions are expected to increase, and negative if the technology is expected to reduce emissions. Three magnitudes of emissions impact are postulated – low, moderate, and high.

## Slide 12: Equity Issues
Shared mobility may be able to address spatial inequality in areas with limited alternatives to private cars, but it needs incentives to locate shared mobility services in underserved areas (Shaheen et al., 2017)
Large variation in the usage of TNCs among the population in different income groups
  According to the 2017 National Household Travel Survey (NHTS) in nine major metropolitan areas, people with annual household income more than $200,000 made 44 TNC trips per year, whereas people with annual household income less than $15,000 made only 6 TNC trips
Shared mobility requires a certain population density to gain business success
  Ridesharing is only available (or efficient) in large cities, e.g. over 50 cities in the US for UberPOOL
  Success of bike sharing and scooter sharing also need high-density communities
Notes: On-demand mobility services that do not convert non-motorized and transit trips to vehicle trips and that promote ridesharing are expected to reduce the total VMT on the roadways, which would result in a reduction in emissions. Alonso-Mora et al. (2017) compared 14,000 New York City taxi trips with a hypothetical ride-sharing operation. They found that 98% of the total taxi trips could be replaced by 3,000 ride-share vehicles with capacity of 4 passengers per vehicle or 2,000 vehicles with 10 passengers per vehicle. Bischoff and Maciejewski (2016) simulated trips from 1.1 million personal vehicles in the city of Berlin, Germany, and found that a fleet of 100,000 shared autonomous vehicles would be able to serve those trips sufficiently. In these simulation studies, no barriers to the adoption of ride-sharing were assumed and, therefore, they represent an ideal scenario.
Evidence of the real-world impacts of TNCs, especially on VMT and congestion, has begun to emerge recently. In the short term, TNCs can incur a significant amount of “deadhead” miles, which are the miles where the driver is driving without any passenger, such as from the drop-off location of one trip to the pick-up location of the next trip (Wenzel et al. 2019). A recent paper (Komanduri et al. 2018) using RideAustin data estimated that 37% of all the miles are due to deadheading. It was estimated to be around 20% in San Francisco (Castiglione et al, 2018) and about 50% in New York City (Schaller, 2018). Castillo et al. (2018) presented a condition of matching failure by TNCs where there is fewer number of available vehicles nearby than there are trip requests. Such failure may contribute to a substantially increased amount of deadhead miles. The number of these empty passenger trips can be reduced significantly by imposing an adaptive matching radii within which the driver supply and trip demand matching must occur (Xu et al., 2019).

## Slide 13: Findings from RideAustin
The net energy impact of TNCs is a combination of:
  Sharing rides
  More fuel-efficient vehicles
  Commute deadheading
  Between-ride deadheading
  Modal shift Estimated
Relative to the distance with passengers, RideAustin drivers traveled 21% more miles just to reach passengers after accepting the request
They took 55% more miles between the end of a ride and the start of the next ride
Source: Wenzel et al. (2019)
Notes: Data on 1.5 million individual rides were used to estimate the additional miles RideAustin drivers travel to reach a rider, as well as the additional miles driven between consecutive rides (referred to as deadheading). Relative to the distance from passenger pick up to drop off, RideAustin drivers traveled 21% more miles just to reach their passenger(s) after accepting the ride request; and drivers traveled an estimated 55% more miles between the end of a ride and the start of the next ride (including the distance traveled to reach the rider who requested the ride) for rides within 60 min of each other. The estimated distance driven by a driver between rides is greater than the measured distance between when a driver accepted a ride request and reached their rider, suggesting that RideAustin drivers are not parking their vehicles but are driving or circling while awaiting their next ride request. However, RideAustin vehicles are more efficient than the average vehicle registered in Austin, partially offsetting the increased energy use from additional VMT.
Out of the total miles driven by RideAustin drivers, 26% correspond to between-ride deadheading and 19% to drivers’ commuting. Three distinct types of drivers are examined, based on the frequency of their driving shifts; the 40% of drivers that are halftime drivers conduct more than half of the ridesourcing rides, and 57% of all ridesourcing VMT, while the 11% of drivers that are fulltime drivers conduct almost 30% of rides with average daily distance of 109 miles. Full-time drivers could complete over 94% of their shifts on a single charge in the latest generation electric vehicles (with around 200 miles real-world range); in addition, 35% of fulltime drivers never exceeded 200 miles in one shift during the study period. In the current situation where the TNC has little control over the number of drivers and vehicles, other than pricing incentives, the supply of drivers may be short of the optimum necessary to
minimize rider wait times and deadheading. When ridesourcing operations are conducted by a centrally managed fleet of automated vehicles, TNCs will have the capability to better balance the supply of vehicles in order to meet the demand for rides, thereby reducing wait times and between-ride deadheading. In addition, a centrally managed fleet of automated vehicles likely will reduce commute deadheading, as well as minimize between-ride deadheading by parking vehicles until their next ride request (Bauer et al., 2018).

## Slide 14: Findings from POLARIS
Source: Auld (2020)
POLARIS is an agent-based modeling framework designed by Argonne National Laboratory
Notes: POLARIS is a high-performance, open-source agent-based modeling framework designed for simulating large-scale transportation systems. The suite includes a discrete-event engine, memory management, visualization capabilities, and an extensible repository of common transportation objects which allows the rapid development of simulation software that satisfy individual project needs. A full-featured transportation systems simulation has been created using this framework and includes traffic flow simulation, activity based demand simulation, model building and analysis geographic information system (GIS) tools, and tools for result analysis. The key feature of the framework is that it allows for developing integrated models. For example, in integrated network-demand model, all of the aspects of travel decisions (departure time, destination choice, planning and rescheduling as well as route choices) can be modeled simultaneously. POLARIS enables the creation of integrated, interoperable, and extensible transportation systems models to evaluate transportation improvements, such as management and operations policies, new mobility options and new technologies. POLARIS is integrated with powertrain simulator Autonomie to perform regional energy use analysis.

## Slide 15: Findings from BEAM
BEAM, developed by Lawrence Berkeley National Laboratory, extends MATSim to enable powerful and scalable analysis of transportation systems.
Source: Needell (2020)
Notes: BEAM stands for Behavior, Energy, Autonomy, and Mobility. The model is being developed as a framework for a series of research studies in sustainable transportation at Lawrence Berkeley National Laboratory and the UC Berkeley Institute for Transportation Studies.
BEAM is an extension to the MATSim (Multi-Agent Transportation Simulation) model, where agents employ reinforcement learning across successive simulated days to maximize their personal utility through plan mutation (exploration) and selecting between previously executed plans (exploitation). The BEAM model shifts some of the behavioral emphasis in MATSim from across-day planning to within-day planning, where agents dynamically respond to the state of the system during the mobility simulation. In BEAM, agents can plan across all major modes of travel including driving, walking, biking, transit, and transportation network companies (TNCs).

## Slide 16: Discussion
Shared your experience with shared mobility, e.g. TNC, ridesharing, car sharing, bike sharing …
Do you think TNCs reduce the emissions or increase the emissions in your city?
What are the potential policies/regulations to guide the development of shared mobility in an eco-friendlier way?

## Slide 17: Research Gaps and Future Directions
High uncertainty in technology deployment and emission impact
  What shared mobility model may succeed in business?
  Synergy with electrification, connectivity and automation
  Change in travel behavior
  Potential policy and its impact
Approaches to evaluate the impact of shared mobility
  Survey from travelers
  Data analysis from existing shared mobility program
  Agent-based models to simulate the technology and behavior
Reduce emissions from shared mobility applications
  Better ridesharing matching
  Fleet electrification
  Shared autonomous fleet
  Synergy with public transit systems

## Slide 18: Take-Home Messages
Shared mobility makes travel more convenient, but the system-level impact (including emission and exposure) may have high uncertainty.
TNCs are the early-adopters of cleaner vehicle technology, but may increase exposure time and VMT.
Ridesharing vs. deadheading is the major challenge in solving the VMT issue in current on-demand mobility services.
Shared autonomous fleet is a key technology in the future to solve the emission and exposure issues in transportation system.
Notes: Promotion of ridesharing and public transportation are the two most effective measures to reduce the negative consequences of on-demand mobility services. Imposing restrictions on single passenger TNC trips can help reduce VMT generated by TNCs. Using on-demand mobility services to provide first-mile and last-mile connections with public transit systems can help promote the use of public transit. On the other hand, multimodal facilities should be modified or upgraded to better accommodate TNC pick-ups and drop-offs. Similarly, better curb space management is needed in city centers and major trip destinations to reduce traffic congestion and idle emissions in those areas, as well as to reduce the wait time where travelers are exposed to traffic-related air pollution.

## Slide 19: List of Abbreviations
CUV: crossover utility vehicle
NHTS: National Household Travel Survey
TNC: transport network companies
VMT: vehicle miles traveled

## Slide 20: References
Alonso-Mora, J., Samaranayake, S., Wallar, A., Frazzoli, E., & Rus, D. (2017). On-demand high-capacity ride-sharing via dynamic trip-vehicle assignment. Proceedings of the National Academy of Sciences, 114(3), 462-467.
Auld, J. (2020). Simulation Model Results for Energy and Mobility Impact of Behavioral Scenarios in POLARIS. 2020 DOE VTO Annual Merit Review. https://www.energy.gov/sites/prod/files/2020/06/f75/eems078_auld_2020_o_4.27.20_249PM_LR.pdf. Accessed on Aug 30, 2020.
Bischoff, J., & Maciejewski, M. (2016). Simulation of city-wide replacement of private cars with autonomous taxis in Berlin. Procedia computer science, 83, 237-244.
Castiglione, J., Cooper, D., Sana, B., Tischler, D., Chang, T., Erhardt, G., Roy, S., Chen, M., & Mucci, A. (2018, October). TNCs & congestion. Draft report, San Francisco County Transportation Authority.
Clewlow, R. R., & Mishra, G. S. (2017). Disruptive transportation: The adoption, utilization, and impacts of ride-hailing in the United States. University of California, Davis, Institute of Transportation Studies, Davis, CA, Research Report UCD-ITS-RR-17-07.
Hall, J. D., Palsson, C., & Price, J. (2018). Is Uber a substitute or complement for public transit?. Journal of Urban Economics, 108, 36-50.
Henao, A., & Marshall, W. E. (2018). The impact of ride-hailing on vehicle miles traveled. Transportation, 1-22.
Hu, L., Dong, J., Lin, Z., & Yang, J. (2018). Analyzing battery electric vehicle feasibility from taxi travel patterns: The case study of New York City, USA. Transportation Research Part C: Emerging Technologies, 87, 91-104.
Komanduri, A., Wafa, Z., Proussaloglou, K., & Jacobs, S. (2018). Assessing the impact of app-based ride share systems in an urban context: Findings from Austin. Transportation Research Record, 2672(7), 34-46.
Needell, Z. (2020). Integrated Mesoscale Urban Systems Modeling with Behavior, Energy, Autonomy, and Mobility model. 2020 DOE VTO Annual Merit Review. https://www.energy.gov/sites/prod/files/2020/06/f75/eems011_needell_2020_o_4.29.20_506PM_JL.pdf. Accessed on Aug 30, 2020.
Schaller, B. (2018). Making Congestion Pricing Work for Traffic and Transit in New York City. Schaller Consulting.
Shaheen, S. Bell, C., Cohen, A., Yelchuru, B. (2017). Travel Behavior: Shared Mobility and Transportation Equity. Federal Highway Administration report PL-18-007.
Shaheen, S. Cohen, A., Randolph, M., Farrar, E., Davis, R., Nichols, A. (2019). Shared Mobility Policy Playbook. Caltrans report. Retrieved from https://escholarship.org/uc/item/9678b4xsWenzel, T., Rames, C., Kontou, E., & Henao, A. (2019). Travel and energy implications of ridesourcing service in Austin, Texas. Transportation Research Part D: Transport and Environment, 70, 18-34.
Xu, Z., Yin, Y., & Ye, J. (2019). On the supply curve of ride-hailing systems. Transportation Research Part B: Methodological.

## Slide 21: Further Readings
Bauer, G. S., Greenblatt, J. B., & Gerke, B. F. (2018). Cost, energy, and environmental impact of automated electric taxi fleets in Manhattan. Environmental science & technology, 52(8), 4920-4928.
Castillo, J. C., Knoepfle, D., & Weyl, G. (2017, June). Surge pricing solves the wild goose chase. In Proceedings of the 2017 ACM Conference on Economics and Computation (pp. 241-242). ACM.
Fulton, L., Mason, J., & Meroux, D. (2017). Three revolutions in urban transportation. Institute for Transportation & Development Policy, Davis, CA.
Greenblatt, J. B., & Shaheen, S. (2015). Automated vehicles, on-demand mobility, and environmental impacts. Current sustainable/renewable energy reports, 2(3), 74-81.
MAPC (2018). Fare Choice: A Survey of Ride-Hailing Passengers in Metro Boston. Metropolitan Area Planning Council Report. Accessed from http://www.mapc.org/wp-content/uploads/2018/02/Fare-Choices-MAPC.pdf Accessed on September 29, 2019.
Nopmongcol, U., Grant, J., Knipping, E., Alexander, M., Schurhoff, R., Young, D., ... & Yarwood, G. (2017). Air quality impacts of electrifying vehicles and equipment across the United States. Environmental science & technology, 51(5), 2830-2837.
Shepardson, D. “Uber resuming self-driving car testing in Pennsylvania”. Dec20, 2018. Accessed on 04.10.2019 from https://www.reuters.com/article/us-uber-selfdriving/uber-resuming-self-driving-car-testing-in-pennsylvania-idUSKCN1OJ1OD.
Slowik, P., Pavlenko, N., & Lutsey, N. (2019). Emerging Policy Approaches to Electrify Ride-hailing in the United States. International Council on Clean Transportation (ICCT) Policy Briefing. Accessed from https://theicct.org/sites/default/files/publications/EV_ridehailing_policy_approaches_20190108.pdf , Accessed September 29, 2019.
Spurlock, C. A., Sears, J., Wong-Parodi, G., Walker, V., Jin, L., Taylor, M., ... & Todd, A. (2019). Describing the users: Understanding adoption of and interest in shared, electrified, and automated transportation in the San Francisco Bay Area. Transportation Research Part D: Transport and Environment.
Tanvir, S., Hao, P., & Boriboonsomsin, K., (2020). Chapter 21 - Emerging transportation technologies and implications for traffic-related emissions, air pollution exposure, and health. Editors: Khreis, H., Nieuwenhuijsen, M., Zietsman, J., Ramani, T. Traffic-Related Air Pollution, Elsevier, 2020, 511-530.